## Slide 1: Surpassing Standards: Elevating Source Water Protection
Elizabeth Crafton, PhD

## Slide 2: Agenda
System Overview
Source Water Protection Plan
Enhanced Best Management Practices
Algaecide Treatment
Remote Sensing

## Slide 3: Core Components to Elevating Source Water Protection
Source Water Protection and Management
HAB
Prevention
Watershed
Lake
Source Water Management
Source Water Protection
External
Internal
Offset anthropogenic impact
Watershed-based
Maintain quality of receiving waters
Buffer impact of external influences
In situ management
Restore or maintain quality of source water

## Slide 4: Background
The Quail Lake System has two primary drinking water reservoirs:
  Quail Creek Reservoir
  Sand Hollow Reservoir
Water for both reservoirs is diverted from the Virgin River at the Quail Creek Diversion Dam
Increases in development and agriculture have caused nonpoint source pollution concerns for the system
Specifically, benthic harmful algal blooms (HABs) have been developing in the Virgin River for decades
  These blooms have more recently made their way into the reservoirs, leading to direct drinking water quality implications

## Slide 5: Source Water Protection Plan (SWPP)
Two main components:
  Prioritized inventory of potential contaminant sources (PCSs)
  Action Plan to address top source water threats
Built off the previous Source Water Protection Plan, which was developed in 2008
  Updated PCS information by conducting a windshield survey
  Updated prioritization input datasets
Highest priority PCSs:
  Abandoned mines
  Campgrounds
  RV Parks
  Vacation rentals
PSOC Priority
Precipitation
Land Cover
Slope
Proximity
Soil Type
Contaminant Type
Structural Integrity
Existing Controls

## Slide 6: Potential for Improvement
The SWPP is a good basis for prioritizing acute contamination concerns
However, less tangible concerns can be missed in contaminant inventories
  Climate change-driven threats (HABs, wildfire)
  Long-term watershed changes (urban development, agriculture)
The following additions to the initial source water protection plan were proposed:
  Water quality modeling to better understand priority areas for nutrient loading
  Additional best management practices (BMPs) to address nutrient loading, urban development, septic systems, and data gaps
  Algaecide treatment for HABs in Sand Hollow Reservoir
  Remote-sensing of upstream reservoir conditions to predict water quality threats

## Slide 7: Nutrient Load Modeling and Enhanced BMPs

## Slide 8: Nutrient Load Modeling
Pollutant Load Estimation Tool
Models such as EPA’s the PLET (Pollutant Load Estimation Tool) can be leveraged to better understand sources of nutrient loading and assess impacts of changing land use over time
  Inputs: Land use/land cover, precipitation, soil characteristics, agricultural animal counts, irrigation, septic systems
  Outputs: Annual loading estimates for total nitrogen, total phosphorus, BOD, and sediment (not considered in this model)
Three subbasins were modeled to assess areas with highest nutrient loading and recommend best management practices (BMPs) based on contributing land use
  Total loading identifies largest loading contributors
  Area-normalized loads help identify target areas for nutrient reduction BMPs
Chart: Load (lbs/year)
| Nitrogen Load | Phosphorus Load | BOD Load
QCR | 25851.2 | 2328.94 | 7021.39
QCDD | 433148.58 | 38527.94 | 126291.85
SHR | 3515.39 | 335.54 | 1588.61
Chart: Load (lbs/ac/year)
| Nitrogen Load | Phosphorus Load | BOD Load
QCR | 0.51919 | 0.046774 | 0.14102
QCDD | 0.70587 | 0.062786 | 0.20581
SHR | 0.39034 | 0.037257 | 0.17639
Total Annual Load
Area-Normalized Annual Load

## Slide 9: Application to Enhanced BMPs
PLET results indicate that forest land contributes most to total nutrient loading
However, pastureland, cropland, and urban land are much larger contributors on a per-acre basis
  A BMP applied to agricultural or urban land result in more nutrient load reduction per acre treated than forest land, lowering costs
Septic systems were also a notable source in model outputs
Couple PLET output with LULC analysis
Recommended BMPs:
  Septic to sewer conversion for the upstream town of Virgin, UT
  Edge-of-field buffers for agricultural land use
  Stormwater management in urban areas
Chart: Load (lbs/year)
| Nitrogen Load | Phosphorus Load | BOD Load
Urban | 7708.23 | 1226.02 | 31363.19
Cropland | 1069.69 | 190.3 | 2241.02
Pastureland | 1531.65 | 126.93 | 4929.24
Forest | 451266.61 | 39453.67 | 95005.88
Chart: Load (lbs/acre/year)
| Nitrogen Load | Phosphorus Load | BOD Load
Urban | 0.68114 | 0.10074 | 2.6042
Cropland | 1.1777 | 0.23063 | 2.4544
Pastureland | 1.4048 | 0.1279 | 4.4741
Forest | 0.55327 | 0.049055 | 0.12059
Total Annual Load
Area-Normalized Annual Load

## Slide 10: Watershed Monitoring
Watershed monitoring can help fill data gaps in nutrient load modeling
  Nutrient or sediment lads caused by factors not considered in model inputs
  Higher spatial resolution for nutrient loads
  Can track seasonal dynamics and long-term watershed changes
Watershed monitoring can also be used to evaluate BMP effectiveness
  Change in nutrient loads downstream of a contaminant source before and after implementation
Monitoring locations were designed to capture major river reaches, critical infrastructure, and key areas for nonpoint sources

## Slide 11: Algaecide Treatment

## Slide 12: Sand Hollow Reservoir: Novel Peroxide Treatment
Benthic algal blooms have been observed in Sand Hollow Reservoir and the upstream Virgin River for decades
The most recent bloom in Sand Hollow Reservoir was observed in October of 2024
Historical algaecide treatments in Sand Hollow Reservoir had used copper
However, due to the ecological impacts of using copper algaecide, WCWCD was interested in exploring peroxide as an alternative solution

## Slide 13: Treatment Planning
Divers surveyed the reservoir pre-treatment to determine areas of growth
  Key Observations: 9 pockets of growth identified, generally occurring at a depth range of 35 – 45 ft
Bathymetry data was combined with survey observations to generate a set of treatment areas (right)
PAK27 dosage:
  Target Concentration: 4 mg/L
  Target Dose: 20 lbs/ac-ft
Application done by boat
  Alternating bands to avoid harming fish populations
  Approximately 20 ft surface broadcast width
Divers completed follow-up survey
Cyanotoxins (anatoxin-a) was detected prior to treatment, was ND at 24 hrs and 7 days post treatment

## Slide 14: Future Preventative Treatments
Preventative treatment was recommended for subsequent seasons
  Easier to address algal blooms before populations have established
  Reduced risk of cyanotoxins or taste and odor (T&O) compounds developing
Temperature monitoring will be used to inform treatment timing
  Target surface temperature of 15 to 18 C
Areas where there has been previous growth should be targeted for preliminary treatment in the following growing seasons
Chart: Month
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2024 | 6.01 | 8.06 | 9.95 | 12.05 | 15.68 | 23.29 | 24.91 | 23.23 | 19.66 | 15.21 | 7.15
2023 | 4.88 | 5.65 | 6.76 | 8.77 | 12.26 | #N/A | 24.12 | 22.47 | 19.05 | 13.96 | 8.37 | 6.19
2022 | 6.2 | 10.19 | 13.48 | 18.04 | 22.39 | 25.09 | 23.34 | 20.67 | 14.29 | 6.47 | 5.53
2021 | 5.44 | 7.69 | 10.15 | 15.06 | 18.75 | 23.13 | 25.24 | 22.74 | 20.25 | 13.26 | 9.55
15 C | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15
18 C | 18 | 18 | 18 | 18 | 18 | 18 | 18 | 18 | 18 | 18 | 18 | 18
Begin Treatment

## Slide 15: Source Water Monitoring

## Slide 16: Monitoring Plan & Water Quality Modeling
A comprehensive routine monitoring plan is necessary for source water protection
  Characterizes baseline conditions and seasonal trends
  Enables proactive implementation of management strategies and monitoring of the success and impacts of those strategies
Recommended an expanded monitoring program in Quail Lake Reservoir and Sand Hollow Reservoir
  Includes water quality profiles, algal enumerations, MIB/geosmin, cyanotoxins, nutrients, and metals
With sufficient monitoring data, a CE-QUAL-W2 model can be constructed to further enhance management decision-making
  Models hydrodynamics and eutrophication processes
  Increases understanding of the underlying causes of HABs and enables prediction of conditions leading to future HAB events

## Slide 17: Enhanced Monitoring: Remote Sensing
Remote-sensing has advantages for HAB monitoring:
  Early detection
  Provides spatial data for targeted algaecide treatments
  Cost-effective
Remote-sensing captured a bloom in an upstream reservoir within the Quail Lake System in October 2022
The reservoir normally releases into Quail Creek and Sand Hollow in October, but operations were halted due to the observed bloom
Chl-a estimates shown were computed using the Normalized Chlorophyll Difference Index (NDCI)
  Computed using the differential reflectance of red and near-infrared wavelengths
  Chlorophyll absorbs red light but reflects/fluoresces in the near-infrared range
9/25/2022
10/01/2022
10/07/2022
10/12/2022
10/14/2022
10/18/2022

## Slide 18: Source Water Protection Has Tangible Impacts
Completion of a SWPP is often considered to be the end product of source water protection
However, there are substantial benefits to expanding source water protection programs:
  Prediction of water quality changes and treatment impacts
  Reduced treatment costs
  Improved data and understanding of watershed conditions
  Reduced contamination risk
  Healthier ecosystems
  Improved public confidence
Modern water treatment challenges make source water protection non-negotiable for utilities:
  Wildfire
  Drought
  Harmful Algal Blooms
  Urbanization

## Slide 19: Summary

## Slide 20: Key Takeaways
SWPPs are great for contextualizing acute risks and prioritizing action
SWPPs are less tangible for dispersed, persistent issues (i.e., wildfire, eutrophication, climate driven changes, flooding, etc)
Augmenting SWPP for dispersed risks is key
Leverage watershed monitoring and modeling
Leverage natural treatment systems to increase biodiversity and habitat conditions
Determine habitat conditions and ecosystem health in the watershed to delineate restoration efforts (i.e., raise ecosystem function)
Eutrophication cannot be reversed through watershed action, source water management must also be included
Actively manage the lakes and reservoirs through in-situ action
Minimize HAB and cyanobacteria dominance
Raise the ecosystem function